# DORMA SPECIFICATION SERVICES

Project

L20/			LOW ENERGY AUTOMATIC SLIDING DOORS

Manufacturers		DORMA UK LTD.

WILBURY WAY, HITCHIN, SG4 0AB.

Tel: 	+44 (0)1462 477 600,

Email: 	Info@dorma-uk.co.uk

Web: 	www.dorma.com

Operating System	DORMA CS80 Magneo Magnetically Driven Automatic Low Energy Sliding Door Operator

      - Electromagnetic automatic low energy sliding door operator consisting of a, Linear motor, power supply and control module incorporated within an aluminium Contour Designed housing

      - Almost silent operation

      - Adjustable opening and closing speed

      - Variable hold open times

      - 3 position program switch (Off, Automatic, permanently open) (Option)

      - Door leaf weights 20kg to 80kg

Drive Cover

      - Contur Drive Cover (always refer to installation guidelines for specific sizes)

      - In wall (58mm x 55mm)

      - On wall (60mm x 75mm)

      - Clear opening widths between 650mm and 1060mm

      - Silver anodised finish

Door leaf options 		(PLEASE SELECT ONE FROM THE FOLLOWING)

      - Door leaf by others

      - Glass clamping rail on wall

      - Glass clamping rail in wall

      - Manet Single point fixing on wall

      - Manet Single point fixing in wall

      - Manet Single point fixing on glass wall

      - Timber Door leaf by others

Activation Options

- Wireless and battery free push button (Option)

- Push and Go (Option)

- Radio remote control (Option)

- Radar Motion detector (Consideration should be given to the suitability of this option due to the low operating speed of the door) (Option)

Power Failure/Fire Alarm	Door reverts to manual operation

Break Out Facility		Not Available

Safety Devices	“Soft Motion” safety automatically reversing the doors if they make contact with an obstruction during the opening or closing cycle

Locking Facility	Fail safe solenoid lock concealed within the operator – Program switch required (Option)

Electrical Requirements 	The electrical contractor shall provide a 240-volt AC mains spur to the right-hand side of the opening above and on the same face that each drive unit is fitted. The spur must be switched and fused with a central flex outlet faceplate. A 10 amp residual circuit breaker at the mains board and a 5-amp fuse at the spur shall protect the circuit.