# DORMA SPECIFICATION SERVICES

Project

Manufacturers		DORMA UK LTD.

WILBURY WAY, HITCHIN, SG4 0AB.

Tel: 	+44 (0)1462 477 600,

Email: 	Info@dorma-uk.co.uk

Web: 	www.dorma.com

Product Reference		 DORMA FSW-G sliding folding glazed partition system

Door leaves, fixed screens

  - Manual top hung sliding folding glass partition system consisting of running track and one of the following configuration options:

    - 2 No. folding panels

    - 4 No. folding panels - 2 left / 2 right

    - 4 No. folding panel in one direction

    - 8 No. folding panels - 4 left / 4 right

    - 6 No. folding panels - 4 one direction / two opposite direction.

    - 2 No. folding panels one direction / 1 No. pivoting end panel

    - 4 No. folding panels one direction / 1 No. pivoting end panel

    - 10mm Toughened safety glass

    - Extruded aluminium profile running track

    - Extruded aluminium top and bottom rails clamped to toughened glass panels comprising of base rails, clip on decorative covers and end caps.

    - Panels secured in closed position by either chute bolts or cylinder locking into floor mounted keeps.

    - End panel hung on top pivot and controlled by DORMA BTS 80 floor spring (Option)

    - Sliding folding panels hung from purpose made roller assemblies consisting of composite multi-directional rollers with non-corrosive engineered carriers and connected by purpose made hinges (and fitted with pulls - option)

    - Aluminium Profile Finish

    - Polyester Powder Coating (Option)

    - Silver Anodised (Option)

    - Stainless Steel (Option)

- Installation carried out by the manufacturer’s approved engineers.